Chapter 16.45	Area’s That Will Provide Multiple Spaces

Sections:

16.45.010	Definition

16.45.015	Subdivisions That Will Provide Multiple Spaces for Recreational Camping Vehicles or Mobile/Manufactured Homes

16.45.020	Review and Approval

16.45.025	Improvements

16.45.030	Final Plat Review

16.45.035	DPHHS License

16.45.040	Design Standards for Subdivision Spaces Created by Rent or Lease

16.45.045	Additional Provisions

16.45.050	Mobile/Manufactured Home Spaces

16.45.055	Streets

16.45.060	Electrical Systems

16.45.065	Gas Systems

16.45.070	Recreational Vehicle Spaces

16.45.075	Density

16.45.010  Definition

A subdivision created by rent or lease, including a mobile home/manufactured home or recreational vehicle park, is any tract of land divided by renting or leasing portions of it.  The land is owned, however, as one parcel under single ownership (which can include a number of persons owning property in common).  Plans, not plats, are submitted to the Subdivision Administrator for review.  The plan shows spaces, not lots.  The plan must comply with applicable zoning.

Enc December 5, 2007, Aff/Renumb/Amend Ord 465 November 6, 2019

16.45.015  Subdivisions That Will Provide Multiple Spaces For Recreational Camping Vehicles Or Mobile/Manufactured Homes

- Recreational Camping Vehicles: Developments which are subject to subdivision review because they will provide two or more spaces for recreational camping vehicles will be reviewed under Section 16.45 DMC Recreational Vehicle Park Standards, below.

- Mobile/Manufactured Homes: Developments which are subject to subdivision review because they will provide two or more spaces for mobile/manufactured homes will be reviewed under Section 16.45 DMC Mobile/Manufactured Home Park Standards, below.

- Subdivisions for Lease or Rent, Generally

  - Buildings created for lease or rent must be subject to DMC Title 16, Chapter 65.  Land subdivision created by rent or lease will be reviewed under the procedures described in 16.25 - Major Subdivisions, or Chapter 16.30 - Minor Subdivisions, as may be appropriate, except that the subdivider shall submit an unsurveyed final plat drawn to scale, rather than a final plat, following the Final Plat procedure in Chapter 16.30.

  - Land subdivisions created by rent or lease are subject to the applicable standards contained in Chapter 16.40.

- The MSPA defines the term “subdivision” to include areas, regardless of their size, that provide or will provide multiple spaces for recreational camping vehicles or mobile homes regardless of whether the spaces will be made available for rent by the general public for a fee.  A development which is a subdivision under the MSPA because it will provide multiple spaces for recreational camping vehicles or mobile homes may also be subject to regulation by the Montana Department of Public Health and Human Services (DPHHS) under Title 50, Chapter 52, MCA, if it will be a “trailer court,” “work camp,” “youth camp,” or “campground” as those terms are defined in Section 50-52-102, MCA.

Enc Ord. 440 April 16, 2014, Aff/Renumb/Amend Ord 465 November 6, 2019

16.45.020  Review And Approval

Subdivisions which will provide multiple spaces for recreational camping vehicles or mobile homes and subdivisions created for rent or lease for rent or lease are exempt from the surveying and filing requirements of the MSPA.  However, these subdivisions must be submitted for review and approved by the governing body before portions of the subdivision may be rented or leased.

- Submittal: The subdivider shall submit a completed application in accordance with Section 16.10.080 DMC and a plan of the proposed development, conforming to the requirements for preliminary plats.

- Review: The procedure used to review subdivisions for rent or lease will depend on the number of spaces within the proposed subdivision.  Proposed subdivisions containing six (6) or more spaces must be reviewed pursuant to Chapter 16.25 DMC of these regulations.  Proposed subdivisions containing five (5) or fewer spaces must be reviewed pursuant to Chapter 16.30 DMC of these regulations.  The subdivider shall submit to the Subdivision Administrator the preliminary plans, profiles, tentative grades, and specifications for proposed improvements.  The plan must show the space layout and the proposed location of the mobile home, recreational vehicle, or other unit on the land included in the plan.

Enc December 5, 2007, Aff/Renumb/Amend Ord 465 November 6, 2019

16.45.025  Improvements

The subdivider shall install all required improvements before renting or leasing any portion of the subdivision.  The governing body or its agents will inspect all required improvements in order to assure conformance with the approved construction plans and specifications.

Enc December 5, 2007, Aff/Renumb/Amend Ord 465 November 6, 2019

16.45.030  Final Plan Review

In lieu of filing a final plat, the subdivider shall submit a final plan to the Subdivision Administrator complying with the requirements of Final Plats in Section 16.35 DMC.  The final plan will be reviewed to assure that it conforms to the approved preliminary plan.  The approved plan must be maintained in the office of the City Clerk and the County Clerk and Recorder.

Enc December 5, 2007, Aff/Renumb/Amend Ord 465 November 6, 2019

16.45.035  DPHHS License

If a subdivision that will provide multiple spaces for recreational camping vehicles or mobile homes is also a “trailer court,” “work camp,” “youth camp,” or “campground” as those terms are defined in Section 50-52-102, MCA, the governing body will not grant final approval of the subdivision until the subdivider obtains a license for the facility from the Montana Department of Public Health and Human Services under Title 50, Chapter 52, MCA.

Enc December 5, 2007, Aff/Renumb/Amend Ord 465 November 6, 2019

16.45.040  Design Standards For Subdivision Spaces Created By Rent Or Lease

Subdivisions created by rent or lease must comply with the provisions of Chapter 16.40, the Design and Improvement Standards, section of these regulations.

Enc December 5, 2007, Aff/Renumb/Amend Ord 465 November 6, 2019

16.45.045  Additional Provisions

The governing body may require provision for:

- storage facilities on the lot or in compounds located within a reasonable distance;

- a central area for storage or parking of boats, trailers, or other recreational vehicles;

- landscaping or fencing to serve as a buffer between the development and adjacent properties;

- an off-street area for mail delivery; and

- street lighting;

- safe school bus loading and unloading zones.

Enc December 5, 2007, Aff/Renumb/Amend Ord 465 November 6, 2019

MOBILE/MANUFACTURED HOME PARK STANDARDS

16.45.050  Mobile/Manufactured Home Spaces

- Mobile/manufactured home spaces must be arranged to permit the safe and practical placement and removal of mobile homes.

- All mobile/manufactured homes must be located at least twenty-five (25) feet from any property boundary line abutting upon a public street or highway right-of-way and at least fifteen (15) feet from other boundary lines of the park.

- The mobile/manufactured home pad must be located at least ten (10) feet from the street that serves it.

- The size of the mobile/manufactured home pad must be suitable for the general market to be served and must fit the dimensions of mobile/manufactured homes anticipated.

- A mobile/manufactured home pad may not occupy more than one-third (1/3) of the area of its space.  The total area occupied by a mobile home and its roofed accessory buildings and structures may not exceed two-thirds (2/3) of the area of a space.

- The governing body may require that the mobile/manufactured home pad be improved to provide adequate support for the placement and tie-down of the mobile home.

- No mobile/manufactured home or its attached structures, such as awnings and carports, may be located within twenty (20) feet of any other mobile home or its attached structures.

- No detached structure, such as a storage shed, may be located within five (5) feet of any mobile/manufactured home or its attached structures.

- A minimum of one (1), off-street parking space, or compliance with applicable zoning, must be provided on or adjacent to each mobile/manufactured home space.  The driveway must be located to allow for convenient access to the mobile/manufactured home, and be a minimum of ten (10) feet wide.

- One guest parking space must be provided for each ten (10) mobile/manufactured home spaces.  Group parking may be provided.

- The limits of each mobile/manufactured home space must be clearly marked on the ground by permanent flush stakes, markers or other suitable means.  Location of space limits on the ground must be approximately the same as those shown on the approved plans.  Precise engineering of space limits is not required either on the plans or on the ground.

- Each mobile/manufactured home must be skirted within thirty (30) days after it is moved to a space within the mobile/manufactured home park.  The skirting must be of a fire-resistant material similar to that of the mobile/manufactured home exterior.

Enc December 5, 2007, Aff/Renumb/Amend Ord 465 November 6, 2019

16.45.055  Streets

Streets within a mobile/manufactured home park must meet the standards specified in Section 16.40.045 DMC Streets and Roads.  Streets must be designed to allow safe placement and removal of mobile homes.

- Streets must be designed to provide safe access to public roads.

- Roads within the mobile/manufactured home park must be designed to provide safe traffic circulation and parking.

- One-way roads must be at least fifteen (15) feet wide; two-way roads must be at least twenty-four (24) feet wide.

Enc December 5, 2007, Aff/Renumb/Amend Ord 465 November 6, 2019

16.45.060  Electrical Systems

Electrical systems must be designed and installed in accordance with the applicable codes adopted by the authority having jurisdiction.  Where the state or other political subdivision does not assume jurisdiction, such installations must be designed and constructed in accordance with the applicable state electrical standards.

Enc December 5, 2007, Aff/Renumb/Amend Ord 465 November 6, 2019

16.45.065  Gas Systems

Gas equipment and installations must be designed and constructed in accordance with the applicable codes adopted by the authority having jurisdiction.  Where the state or other political subdivision does not assume jurisdiction, such installation must be designed and constructed in accordance with the applicable provisions of the “National Fuel Gas Code” (NFPA Pamphlet 54-1981.and the “Standard for the Storage and Handling of Liquefied Petroleum Gases” (NFPA Pamphlet 58-1981).

Enc December 5, 2007, Aff/Renumb/Amend Ord 465 November 6, 2019

16.45.070  Recreational Vehicle Spaces

- Spaces in recreational vehicle parks must be arranged to allow for the safe movement of traffic and access to spaces.

- Roads within recreational vehicle parks must be designed to provide safe traffic circulation and parking.

- Recreational vehicles must be separated from each other and from other structures by at least twenty (20) feet.  Any accessory structures such as attached awnings must, for purposes of this separation requirement, be considered part of the recreational vehicle.

- No recreational vehicle space may be located less than twenty-five (25) feet from any public street or highway right-of-way.

- Streets must be designed to provide safe access to public roads.

Enc December 5, 2007, Aff/Renumb/Amend Ord 465 November 6, 2019

16.45.075  Density

The density of a recreational vehicle park must not exceed twenty-five (25) recreational vehicle spaces per acre of gross site area.

Enc December 5, 2007, Aff/Renumb/Amend Ord 465 November 6, 2019